## Slide 1: Water Level Control System
(Automatic and Manual)

## Slide 2
Name | Roll Number
D M Shaahid | CB.EN.U4ECE21011
D Santhosh | CB.EN.U4ECE21012
N Sumanth | CB.EN.U4ECE21033
P Ganesh | CB.EN.U4ECE21036

## Slide 3: Introduction
A Water level control system is a device or mechanism that automatically monitors and regulates the level of water In the tank, reservoir, or any other water storage system
Importance of Water Level Control
Prevent Overflow and Flooding.
Ensures optimal water usage.
Maintains consistent water pressure.
Protects Equipment from damage.
Enables efficient water management.
What is Water Level Control system ?

## Slide 4: Literature Survey
Title of Literature | Source Type | Authors | Publication Year | Key Insights
Fundamentals of Digital Logic with Verilog Design | TextBook | Stephen Brown and Zvonko Vranesic | 2002 | Combinational circuits; Flip-Flops, Registers, Counters; 3. Synchronous Sequential Circuits
Microelectronic Circuits | TextBook | Adel S. Sedra Kenneth C. Smith | 2015 | Signal Generators and Waveform Shaping Circuits

## Slide 5: System Components
555 Timer(IC555) | 1
3⤫8 decoder (IC74138) | 1
Relay(5V) | 1
Resistors (68K Ω,39K Ω,1K Ω) | 1,1,4
Capacitors (10nF,100nF,1µF) | 2,1,1
Float switches | 5
Breadboard | 2
Connecting wires | As Requried
AND Gate (IC7408) | 1
NOR Gate(IC7402) | 1
JK flipflop(IC74112) | 2
4⤫1 MUX(IC74153) | 2
NOT Gate(IC7404) | 1

## Slide 6: Explanation
Our project is based on a “Water Level Control System”.
The water is controlled in two ways
Automatic Method
Manual Method.
Cont…

## Slide 7
A Water Level Control System is a technological solution designed to automatically regulate and maintain the water level within a specific range or at a predetermined set point.
This system typically employs float switches to detect the water level and actuator (Relay) to adjust the flow of water accordingly.
It is commonly used in applications where precise and continuous control of water levels is required, such as in industrial processes, irrigation systems, and water treatment plants.
Water Level Control System:
Cont…
1. Automatic :

## Slide 8
The manual method of controlling water levels is designed for users who prefer to operate the system manually, without relying on automated controls.
This method provides users with the flexibility to control the water level according to their specific needs and preferences, but it may require more attention and effort compared to automated systems.
2. Manual Method:

## Slide 9: Simulation

## Slide 10
  If switch is in LOW it depicts automatic mode and when HIGH it depicts Manual mode.

## Slide 11: Working
Cont…
  Now This Automatic/ Manual switch acts as select line to the encircled Multiplexers (2⤫1).

## Slide 12: Manual Mode
 | J | K
On | 1 | 0
Off | 0 | 1

## Slide 13: Working
  In automatic mode, the NOR GATE output and the output from the 4⤫1 MUX serve as inputs to MUX 1 and MUX 2, respectively.
  The outputs of MUX 1 and MUX 2 then become the inputs for the JK flip-flop.

## Slide 14: Working
  By Default the inputs fed to JKFF 1 is J = 1 and K = 1. Clock is assigned by the LEVEL SELECTOR which intact given by the user.
Cont…

## Slide 15: Working
Cont…
  The output of JKFF1 is connected as the input to JKFF2, further the outputs of JKFF1 and JKFF2 are connected as select lines to the mux(4⤫1).

## Slide 16: Working
Cont…
  Similarly, the same outputs of JKFF1 and JKFF2 are connected as inputs to the 2×4 Decoder in order to reflect the input provided by the user at the LEVEL SELECTOR.

## Slide 17: Working
Cont…
  These float switches are connected to 4⤫1 mux.
  Float switches facilitate automatic tank filling according to the desired input from the user.

## Slide 18: Working
Cont…
  When the user selects Automatic mode, if the water level drops below a certain threshold (set at 25%), the motor turns on automatically.

## Slide 19
UPPER THRESHOLD% | LOWER THRESHOLD% | J | K
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 0 | 1
J = Upper Threshold NOR Lower Threshold
K = Upper Threshold

## Slide 20: Working
  Theoretical calculation
  T = 0.7 ⤫ (39K + 2(68K)) ⤫ 100n
    T = 0.01225 sec
    f = 81.63 Hz

## Slide 21: Working
  When the water level falls below 25%, a HIGH signal is fed to the ‘J’ of the JK flip-flop.
  Similarly the output of 4⤫1 is fed to ‘K’ of the JK flip-flop.

## Slide 22: Benefits
Improved Efficiency :
Water level control systems optimise water usage by maintaining the desired water level automatically. This ensures that water is not wasted or overused, leading to increased efficiency in water management.
Reduced Waste :
By accurately controlling the water level, these systems prevent overflows and leaks, reducing water wastage. This not only helps conserve water resources but also minimizes water-related damages and costs.
Increased Safety :
Water level control systems ensure the safety of water-related processes and equipment. By maintaining the optimal water level, potential hazards such as flooding, equipment damage, and accidents are prevented, creating a safer environment.

## Slide 23: References
  LM555 Timer
  https://www.ti.com/lit/ds/symlink/lm555.pdf?ts=1710064034359&ref_url=https%253A%252F%252Fwww.google.com%252F
  Relay Switch
  https://components101.com/switches/12v-relay
  JK Flip-Flop
  https://www.ti.com/lit/ds/symlink/sn54ls76a.pdf?ts=1710050565943&ref_url=https%253A%252F%252Fwww.google.com%252F
  NOR Gate
  https://www.ti.com/lit/ds/symlink/sn74ahc1g02-ep.pdf?ts=1710149482660&ref_url=https%253A%252F%252Fwww.google.com%252F

## Slide 24: References
  NOT Gate
  https://www.ti.com/lit/ds/symlink/sn74lvc1g04.pdf?ts=1710149517735&ref_url=https%253A%252F%252Fwww.google.com%252F
  AND Gate
  https://www.ti.com/lit/ds/symlink/sn74lvc2g08-ep.pdf?ts=1710149410655&ref_url=https%253A%252F%252Fwww.google.com%252F
  4⤫1 Mux
  https://www.ti.com/lit/ds/symlink/sn54als153.pdf?ts=1710149278799&ref_url=https%253A%252F%252Fwww.google.com%252F
  2⤫1 Mux
  https://www.ti.com/lit/ds/symlink/sn74lvc2g157.pdf?ts=1710149327154&ref_url=https%253A%252F%252Fwww.google.com%252F

## Slide 25
THANK YOU